## Slide 1: SDN/OpenFlow/NFV Workshop

## Slide 2: Yi-Sung Chiu
NCTU major in SDN/NFV
ONOS, free5GC contributor
Experience
  Attended ONF brigade in 2018 and 2019

## Slide 3: Agenda
Software-Defined Network (SDN)
Open vSwitch (OvS) and Mininet
  Try Mininet/OvS Command
  Custom Mininet Topology
Ryu and OpenFlow Rule
  Run Ryu Built-in Application
  Capture OpenFlow Packet
  Install OpenFlow Rule with REST
Ryu Application
  Path Service
  Proxy ARP

## Slide 4: Before We Start
Please make sure you run up our provided VM
Install the Github repository used for exercises in this workshop
  https://github.com/stevenchiu30801/cht-workshop

## Slide 5: Software-Defined Network (SDN)
Introduction

## Slide 6: SDN Architecture
Network intelligence is (logically) centralized with a global view of network
Underlying infrastructure is abstracted for applications and network services
Network control become directly programmable

## Slide 7: Open vSwitch (OvS) and Mininet
Introduction

## Slide 8: Why Open vSwitch?
Hypervisors need to bridge traffic between VMs and with outside world
  The built-in L2 switch (the Linux bridge) is used
In multi-server virtualization deployment, the Linux bridge is not well suited
  Highly dynamic end-points
  Maintenance of logical abstractions
  (sometimes) Integration with or offloading to special purpose switching hardware
Notes: The mobility of state/Responding to network dynamics
All network state should be easily identifiable and migratable between different hosts.
Configuration and live network state could be migrated easily with existence of OvS database.
Also, with the support of OpenFlow protocol, network control becomes directly programmable.

## Slide 9: Open vSwitch (OvS)
A software-implemented virtual switch
Support many legacy network protocol
  IPv6
  Multiple tunneling protocols (GRE, VXLAN, etc.)
  Etc.
Support latest OpenFlow protocol (version 1.5)

## Slide 10: Mininet Overview
A network emulator which creates a virtual network on a single machine
  Including virtual hosts, switches, controllers, and links
Provides a simple network testbed for developing SDN applications

## Slide 11: How Mininet Works?
Host
  Created with network namespace, a lightweight virtualization feature, to provide separated network environment
Switch
  Created with Open vSwitch
  All switches are placed in root namespace by default
Link
  Use virtual Ethernet (veth) pairs
Controller
  Use OpenFlow reference controller which implements a bridge/learning switch
  Does not implement a spanning-tree protocol by default
Notes: OpenFlow reference controller in Mininet
https://github.com/mininet/mininet/wiki/FAQ#why-does-my-controller-which-implements-an-ethernet-bridge-or-learning-switch-not-work-with-my-network-which-has-loops-in-it-i-cant-ping-anything
Mininet currently depends on the Linux kernel

## Slide 12: Open vSwitch (OvS) and Mininet
Try Mininet/OvS Command

## Slide 13: Run Mininet
Start a minimal topology
Change topology size and type
Cleanup Mininet
$ sudo mn
$ sudo mn --topo single,3 # single switch with three hosts attached
$ sudo mn --topo tree,2 # one switch connected to two edge switches and \
two hosts attached to each of edge switches
$ sudo mn -c

## Slide 14: Mininet CLI Commands
Display Mininet CLI commands
Display nodes
Display links
mininet> help
mininet> nodes
mininet> net

## Slide 15: Interact with Mininet Hosts and Switches (I)
Show network interface on host h1
Ping host h2 from host h1
Test connectivity between all hosts
mininet> h1 ifconfig
mininet> h1 ping -c 1 h2
mininet> pingall # This is a Mininet built-in command

## Slide 16: Interact with Mininet Hosts and Switches (II)
Run a simple web server and client
XTerm Display
For more Mininet commands, Please refer to http://mininet.org/walkthrough/.
mininet> h1 python -m SimpleHTTPServer 80 &
mininet> h2 wget -O - h1
…
mininet> h1 kill %python
mininet> xterm h1 # This is a Mininet built-in command

## Slide 17: It’s Your Turn
Start a Mininet topology
Display node and link information
Ping a host from another to check connectivity

## Slide 18: OvS Commands
ovs-vsctl
  Utility for querying and configuring ovs-vswitchd
  http://www.openvswitch.org/support/dist-docs/ovs-vsctl.8.txt
ovs-ofctl
  Administer OpenFlow switches
  http://www.openvswitch.org/support/dist-docs/ovs-ofctl.8.txt
ovs-dpctl
  Administer Open vSwitch datapaths
  http://www.openvswitch.org/support/dist-docs/ovs-dpctl.8.txt
ovs-appctl
  Utility for configuring running Open vSwitch daemons
  http://www.openvswitch.org/support/dist-docs/ovs-appctl.8.txt
Notes: Also refer to http://therandomsecurityguy.com/openvswitch-cheat-sheet/.

## Slide 19: ovs-vsctl (I)
Print version information of Open vSwitch
Print a brief overview of switch database contents
Print a list of configured bridges and ports on a specific bridge
mininet> sh ovs-vsctl -V # Or `s1 ovs-vsctl -V`
mininet> sh ovs-vsctl show
mininet> sh ovs-vsctl list-br
mininet> sh ovs-vsctl list-ports <bridge> # e.g. `s1 ovs-vsctl list-ports s1`

## Slide 20: ovs-vsctl (II)
Initialize Open vSwitch database
Create a new bridge and a new port on a specific bridge
Set one or more configured controllers and controller failure mode
mininet> sh ovs-vsctl init
mininet> sh ovs-vsctl add-br <bridge>
mininet> sh ovs-vsctl add-port <bridge> <port>
mininet> sh ovs-vsctl set-controller <bridge> <target…>
mininet> sh ovs-vsctl set-fail-mode <bridge> standalone|secure

## Slide 21: ovs-ofctl (I)
Print information on switch flow tables and ports
Print all flow entries in switch’s tables
Add flow entries to switch’s table
mininet> sh ovs-ofctl show
mininet> sh ovs-ofctl [-O version] dump-flows <bridge> # e.g. `sh ovs-ofctl -O OpenFlow13 dump-flows s1`
mininet> sh ovs-ofctl add-flow <bridge> <flow>

## Slide 22: It’s Your Turn
Start a minimal Mininet topology
Install a flow entry using normal non-OpenFlow pipeline and outputting
Check connectivity
Delete the flow entry
Install flow entries matching Ethernet destination address and output to port
mininet> sh ovs-ofctl add-flow s1 actions=normal
mininet> sh ovs-ofctl del-flows s1
mininet> sh ovs-ofctl add-flow s1 eth_dst=f6:db:e3:88:de:2c,actions=output:1

## Slide 23: Questions
How to perform multicasting?
How about priority of flow entries?
How to drop packets?

## Slide 24: Open vSwitch (OvS) and Mininet
Custom Mininet Topology

## Slide 25: Custom Mininet Topology
self.addSwitch()
self.addHost()
self.addLink()

## Slide 26: It’s Your Turn
Try to construct a 2x2 leaf-spine topology as follow
Spine Switch
Leaf Switch
Please check cht-workshop

## Slide 27: Questions
Can all hosts reach to each other?
  If not, why?

## Slide 28: Ryu and OpenFlow Rule
Introduction

## Slide 29: Ryu
SDN Framework
  Python library for SDN
  Apache v2 license
Features
  OpenFlow
    Version 1.0, 1.2, 1.3, 1.4
  Parsing and building various protocols packets
    IP, TCP, UDP, MPLS, OSPF, PBB, etc
  BGP, VRRP, BFD, BMP…

## Slide 30: Ryu Architecture

## Slide 31: OSI Layers
Physical
Data-Link
Network
Transport
Session
Presentation
Application

## Slide 32: Each Layer Network Devices
Physical -> hub
Data-Link -> switch
Network -> router
Transport -> firewall
Session
Presentation
Application -> DPI, L7 firewall

## Slide 33: OpenFlow Support Layer
Physical
Data-Link
Network
Transport
Session
Presentation
Application -> DPI, L7 firewall

## Slide 34: How OpenFlow Works?[5]

## Slide 35: How OpenFlow Works?[5]

## Slide 36: How OpenFlow Works?[5]

## Slide 37: How OpenFlow Works?[5]

## Slide 38: How OpenFlow Works?[5]

## Slide 39: How OpenFlow Works?[5]

## Slide 40: How OpenFlow Works?[5]

## Slide 41: How OpenFlow Works?[5]

## Slide 42: How OpenFlow Works?[5]

## Slide 43: How OpenFlow Works?[5]

## Slide 44: How OpenFlow Works?[5]

## Slide 45: How OpenFlow Works?[5]

## Slide 46: How OpenFlow Works?[5]

## Slide 47: OpenFlow Event
Controller to Switch messages
  Features
  Modify-State
  Packet-out
  Configuration, Read-State, Barrier, Role-Request, Asynochronous-Configuration
Switch to Controller Asynchronous Messages
  Packet-In
  Flow Removed
  Port Status
  Error
Switch to Controller Symmetric Messages
  Hello
  Echo Request / Reply
  Experimenter

## Slide 48: OpenFlow Match-field[6]

## Slide 49: OpenFlow Actions [6]

## Slide 50: OpenFlow Other Functions
Group
Queue
Meter

## Slide 51: Ryu and OpenFlow Rule
Run Ryu Built-in Application

## Slide 52: Built-in Application
ryu.app.ofctl
  Provides a convenient way to use OpenFlow messages synchronously.
    Load Automatically
ryu.app.ofctl_rest
  Provides REST APIs for retrieving the switch stats and Updating the switch stats.
  Reference: https://ryu.readthedocs.io/en/latest/app/ofctl_rest.html
ryu.app.simple_switch_13
  Performs MAC/source learning mechanism for packet forwarding.
ryu.app.gui_topology.gui_topology
  Provides topology visualization.
  Please add --observe-links flags to make Ryu discover links between devices
  GUI can be access at http://<ryu-ip>:8080 on your web browser

## Slide 53: It’s Your Turn (I)
Run Ryu built-in Simple Switch 13 application
Run a Mininet topology (without loop) and connect it to Ryu
Check if OvS in Mininet is connected to Ryu
Check connectivity
Dump flow entries on OvS and find details of match/action
$ sudo mn --controller=remote,ip=127.0.0.1,port=6653
$ ryu-manager ryu.app.simple_switch_13

## Slide 54: It’s Your Turn (II)
Run Ryu built-in topology viewer application
Run a Mininet topology and connect it to Ryu
Check GUI on web browser
$ sudo mn --topo=tree,2 --controller=remote,ip=127.0.0.1,port=6653
$ ryu-manager --observe-links ryu.app.gui_topology.gui_topology

## Slide 55: Ryu and OpenFlow Rule
Run OpenFlow in Real Switch

## Slide 56: Pica8 OpenFlow Switch [7]
Porting the OpenVSwitch into the real switch with hardware ASIC accelerate.
Provides both L2/L3 legacy mode or OpenFlow mode
  Use #picos_boot to switch
Some commands are different from mininet
  Add Bridge
    #ovs-vsctl add-br br0 -- set bridge br0 datapath_type=pica8
  Add Ports
    #ovs-vsctl add-port br0 ge-1/1/1 -- set interface ge-1/1/1 type=pica8
  Set controller
    #ovs-vsctl set-controller br0 tcp:192.168.100.1:6633

## Slide 57: Ryu and OpenFlow Rule
Capture OpenFlow Packet

## Slide 59: It’s Your Turn
Run Ryu built-in Simple Switch application
Run a Mininet topology (without loop) and connect it to Ryu
Open Wireshark and start to capture packets on loopback interface
Ping a host from another one
Observe OpenFlow packets captured by Wireshark

## Slide 60: Ryu and OpenFlow Rule
Install OpenFlow Rule with REST

## Slide 61: It’s Your Turn (I)
Run Ryu built-in REST API application
Run a minimal Mininet topology and connect it to Ryu
Check connectivity

## Slide 62: It’s Your Turn (II)
Install flow entry with REST API
Check connectivity
Dump flow entries on OvS
$ curl -X POST http://localhost:8080/stats/flowentry/add -d '{ \
"dpid": 1, \
"priority": 1000, \
"actions": [ { "type": "OUTPUT", "port": "NORMAL" } ] \
}'

## Slide 63: It’s Your Turn (III)
Delete flow entry with REST API
Check connectivity
Dump flow entries on OvS
$ curl -X POST http://localhost:8080/stats/flowentry/delete -d '{ \
"dpid": 1, \
"priority": 1000, \
"actions": [ { "type": "OUTPUT", "port": "NORMAL" } ] \
}'

## Slide 64: It’s Your Turn (IV)
Install flow entry with REST API
Check connectivity
Dump flow entries on OvS
$ curl -X POST http://localhost:8080/stats/flowentry/add -d '{ \
"dpid": 1, \
"priority": 1000, \
"match": { \
"eth_dst": "f6:db:e3:88:de:2c" \
}, \
"actions": [ { "type": "OUTPUT", "port": 1 } ] \
}'

## Slide 65: Ryu Application Practice
Path Service and Proxy ARP

## Slide 66: It’s Your Turn
Path Service – detect a network topology and find path from host to host.
Proxy ARP – Implement proxy arp service in controller
Run your own application
Please check cht-workshop
$ ryu-manager <app-file-path>

## Slide 67: Reference
[1] “Software-Defined Networking (SDN) Definition.” Open Networking Foundation. [Online]. Available: https://www.opennetworking.org/sdn-definition/
[2] “Why Open vSwitch?” Linux Foundation. [Oneline]. Available: https://github.com/openvswitch/ovs/blob/master/Documentation/intro/why-ovs.rst
[3] “Open vSwitch.” Linux Foundation. [Online]. Available: http://www.openvswitch.org/
[4] “Mininet.” Mininet Team. [Online]. Available: http://mininet.org/
[5] “Introduction to OpenFlow.” David Mahler. [Online]. Available: https://www.youtube.com/watch?v=l25Ukkmk6Sk&t=257s
[6] “SDN/OpenFlow/Flowprogrammable” Available: http://flowgrammable.org/sdn/openflow/
[7] “Pica8 PicOS Configuration Guide” Available: https://docs.pica8.com/display/PicOS21119sp/PICOS+2.11.19+Configuration+Guide